## Slide 1
ScaleHD: Robust Brain-Inspired Hyperdimensional Computing via Adapative Scaling
Sizhe Zhang*, Mohsen Imani#, Xun Jiao*
*Villanova University, #UC Irvine

## Slide 2: Outline
HD Computing Background
  Robustness of HD Computing
Proposed Approach
  ScaleHD
Experimental Results
  Enhanced Robustness
Conclusion

## Slide 3: Outline
HD Computing Background
  Robustness of HD Computing
Proposed Approach
  ScaleHD
Experimental Results
  Enhanced Robustness
Conclusion

## Slide 4: Brain-Inspired HD Computing (HDC)
Tang, Evelyn, et al. "Effective learning is accompanied by high-dimensional and efficient representations of neural activity." Nature neuroscience 22.6 (2019): 1000-1009.
[-1, +1, +1, -1, -1, +1, … ]
[+1, +1, -1, +1, -1, -1, … ]
Dog vector
Cat vector
HD Computing (HDC)
High-dimensional vector (HV)-based computing
One/Few-shot learning
Small model size
Energy-efficient/real-time/robust processing
High parallelism

## Slide 5: HDC Process: Encoding, Training, Inference
HDC
Encoding
Dog
Cat
?
[1 -1 1 … -1 1]
[1 1 -1 … -1 -1 ]
[-1 -1 1 … 1 -1]
Dog HV
Cat HV
Query (?) HV
…
…
HDC
Training
Similarity
Check
It is a dog!
(Because query HV is
most similar to dog HV.

## Slide 6: HDC Basics: HVs and Operations
Cosine similarity
Hypervectors (HVs) are the basic elements of HDC
  High-dimensional (~10,000)
  (pseudo)-random with i.i.d components
  [-1, +1, +1, -1, -1, +1, … ]
HV Operations:
Addition
Multiplication
Permutation

## Slide 7: Robustness of HDC to Hardware Errors
HDC is already implemented in multiple HW platforms (FPGA, ASIC, GPU, emerging memory, etc).
Source of hardware errors
  Voltage scaling
  Soft errors
  Variations, non-idealities …
Zhang et al, DATE 2022
0
1
0
1
0
1
0
0
0
0
0
0
0
1
0
1
Bits Flip

## Slide 8: Our Previous Work on HDC Robustness
Sizhe Zhang, Ruixuan Wang, Jeff (Jun) Zhang, Abbas Rahimi, Xun Jiao, “Assessing Robustness of Hyperdimensional Computing Against Errors in Associative Memory”, ASAP 2021.
  Characterize error impact
Sizhe Zhang, Ruixuan Wang, Dongning Ma, Jeff Jun Zhang, Xunzhao Yin, Xun Jiao, “Energy-Efficient Brain-Inspired Hyperdimensional Computing Using Voltage Scaling”, DATE 2022 (best paper candidate).
  Extra error correction hardware (Razor)
Notes: Can we have approaches that have less overhead?

## Slide 9: Outline
HD Computing Background
  Robustness of HD Computing
Proposed Approach
  ScaleHD
Experimental Results
  Enhanced Robustness
Conclusion

## Slide 10: Key Observation
Bit flip has less impact with larger value (same data-width).
Good news for HDC:
  (1) Linear scale do not affect HDC inference (Cosine Similarity)
  (2) Lots of spare space (empty bit).
3.4X
0.85X
INT32 (-2.1E+09, 2.1E+09)

## Slide 11: ScaleHD Approach
Three levels of ScaleHD
  Global scaling
  Class scaling
  Class + Clip scaling
Apply once after training and before deploy (Overhead can be ignored)

## Slide 12: Global-ScaleHD
Find the max value among all class HVs
Find the max value of the given bit representation (2^32)
Calculate the ratio
Scale up all class HVs with the calculated ratio
Data distribution histogram with Global-ScaleHD
Original distribution histogram of class HVs

## Slide 13: Class-ScaleHD
Each class HV is independent with each other
Different Class HV has different value distribution
Find extreme value of each class HV and scale individually

## Slide 14: (Class+Clip)-ScaleHD
Clip partial extreme values
Perform class HV scale after clip
Find the balance clip value between accuracy and clip value for each dataset
 | Number clipped values | Robustness enhancement | Accuracy
Larger clip value | ↑ | ↑ | ↓
Smaller clip value | ↓ | ↓ | ↑

## Slide 15: (Class+Clip)-ScaleHD
Perform experiments across different models to find the suitable clip value for each application (less than 1% accuracy loss)

## Slide 16: Outline
HD Computing Background
  Robustness of HD Computing
Proposed Approach
  ScaleHD
Experimental Results
  Enhanced Robustness
Conclusion

## Slide 17: Similarity vs. Error Rate
Similarity between error-injected model vs. original model
  More similar  less impact of errors

## Slide 18: Accuracy vs. Error Rate
Simulation Setup
  32/16/8-bit integer
  Four datasets
  Average of 10 Times
Result
  Robustness Enhancement: (Clip+Class) ScaleHD > Class ScaleHD > Global ScaleHD
  Around 100X~10000X robustness enhancement

## Slide 19: Increased Robustness -> Improved Efficiency
22nm SRAM Simulation
Lower voltage cause higher bit error rate but save more energy
Less than 1% accuracy loss

## Slide 20: Conclusion
HDC is vulnerable to hardware errors.
ScaleHD enhances the robustness of HDC to memory errors by scaling up HV values.
  ScaleHD has three levels of scaling: global, class, class+clip.
ScaleHD achieves up to 10,000X robustness enhancement.

## Slide 21: Thank you!